## Slide 1
Restoration and development of Arm's Java-based LEGv8 ISA simulator
Trieste, 01 September 2024
Department of Engineering and Architecture
Graduating student - Simone Deiana
Supervisor - Alberto Carini

## Slide 2
INTRODUCTION
Restoration and development of
Arm's Java-based LEGv8 ISA simulator​

## Slide 3
INTRODUCTION
Restoration and development of
Arm's Java-based LEGv8 ISA simulator​

## Slide 4
INTRODUCTION
Restoration and development of
Arm's Java-based LEGv8 ISA simulator​

## Slide 5
WHAT IS LEGv8?
Restoration and development of
Arm's Java-based LEGv8 ISA simulator​

## Slide 6
WHAT IS LEGv8?
Peg Skorpinski, CC BY-SA 3.0 <https://creativecommons.org/licenses/by-sa/3.0>, via Wikimedia Commons
Eric Chan, CC BY 2.0 <https://creativecommons.org/licenses/by/2.0>, via Wikimedia Commons
John L. Hennessy
David A. Patterson
AN ISA FOR LEARNING COMPUTER ARCHITECTURES
From Computer Organization and Design ARM Edition: The Hardware Software Interface - Patterson, D.A. and Hennessy, J.L.

## Slide 7
WHAT IS LEGv8?
As simple as it can be...
… but with a modern design
Heavily inspired by ARMv8, almost a "subset"
THE DESIGN PHILOSOPHY

## Slide 8
WHAT IS LEGv8?
64-bit addresses
Harvard model
THE MEMORY

## Slide 9
WHAT IS LEGv8?
32 64-bit "X" integer registers
32 64-bit "D" floating-point registers
32 32-bit "S" floating-point "registers"
THE REGISTERS

## Slide 10
WHAT IS LEGv8?
64-bit integer and IEEE-754 floating-point arithmetic
Designed and optimized for pipelined execution
THE INSTRUCTIONS

## Slide 11
WHAT IS LEGv8?
THE DATAPATH
From Computer Organization and Design ARM Edition: The Hardware Software Interface - Patterson, D.A. and Hennessy, J.L.

## Slide 12
WHAT IS LEGv8?
THE DATAPAH
INSTRUCTION MEMORY
From Computer Organization and Design ARM Edition: The Hardware Software Interface - Patterson, D.A. and Hennessy, J.L.

## Slide 13
WHAT IS LEGv8?
THE DATAPATH
REGISTERS AND CONTROL UNIT
From Computer Organization and Design ARM Edition: The Hardware Software Interface - Patterson, D.A. and Hennessy, J.L.

## Slide 14
WHAT IS LEGv8?
THE DATAPATH
ALU
From Computer Organization and Design ARM Edition: The Hardware Software Interface - Patterson, D.A. and Hennessy, J.L.

## Slide 15
WHAT IS LEGv8?
THE DATAPATH
DATA MEMORY
From Computer Organization and Design ARM Edition: The Hardware Software Interface - Patterson, D.A. and Hennessy, J.L.

## Slide 16
WHAT SIMULATOR, AND WHY?
Restoration and development of
Arm's Java-based LEGv8 ISA simulator

## Slide 17
WHAT SIMULATOR, AND WHY?
NO HARDWARE FOR LEGv8 => NEED A SIMULATOR
Michael H. („Laserlicht“) / Wikimedia Commons

## Slide 18
WHAT SIMULATOR, AND WHY?
BUT WHICH ONE?

## Slide 19
WHAT SIMULATOR, AND WHY?
THE PROBLEM:
NO SOFTWARE CAN YET SIMULATE THE ENTIRE LEGv8 ISA!

## Slide 20
WHAT SIMULATOR, AND WHY?
THE SOLUTION:
Write one from scratch
OR (BETTER)​
Improve one that already exists

## Slide 21
WHAT SIMULATOR, AND WHY?
ARM HAS OFFICIALLY MADE A LEGv8 SIMULATOR
THE GOOD NEWS

## Slide 22
WHAT SIMULATOR, AND WHY?
WHAT STANDS OUT:
Written in Java (high level, extensible)
Distributed as a web application
Nice, functional UI
Closely follows the textbook

## Slide 23
WHAT SIMULATOR, AND WHY?

## Slide 24
FIXING AND RESTORING THE SIMULATOR
STRUCTURE OF THE SIMULATOR
CPU
MEMORY
EXECUTION MODE
CODE PARSER/LEXER
INSTRUCTION

## Slide 25
WHAT SIMULATOR, AND WHY?
IT'S INCOMPLETE
AND BROKEN
THE BAD NEWS

## Slide 26
FIXING AND RESTORING
THE SIMULATOR
Restoration and development of
Arm's Java-based LEGv8 ISA simulator​

## Slide 27
FIXING AND RESTORING THE SIMULATOR
COMPARISONS DON'T WORK!
No "if-else" conditionals
No "switch-case" conditionals
No "while" loops
No "for" loops

## Slide 28
THE COMPARISON BUG
FIXING AND RESTORING THE SIMULATOR
X0 = 1, X1 = 2

## Slide 29
THE COMPARISON BUG
FIXING AND RESTORING THE SIMULATOR
COMPARE X0 WITH X1

## Slide 30
THE COMPARISON BUG
FIXING AND RESTORING THE SIMULATOR
1 <= 2 ?
OF COURSE, LET'S JUMP!

## Slide 31
THE COMPARISON BUG
FIXING AND RESTORING THE SIMULATOR
...OR NOT

## Slide 32
BRANCH AND LINKS DON'T WORK!
void subroutine(arg1, ...)
float function(arg1, ...)
CAN'T REUSE CODE
FIXING AND RESTORING THE SIMULATOR

## Slide 33
THE BRANCH AND LINK BUG
FIXING AND RESTORING THE SIMULATOR

## Slide 34
THE BRANCH AND LINK BUG
FIXING AND RESTORING THE SIMULATOR

## Slide 35
THE BRANCH AND LINK BUG
FIXING AND RESTORING THE SIMULATOR

## Slide 36
THE BRANCH AND LINK BUG
FIXING AND RESTORING THE SIMULATOR

## Slide 37
IT DOESN'T GO BACK!
THE BRANCH AND LINK BUG
FIXING AND RESTORING THE SIMULATOR
WE SHOULD BE HERE!

## Slide 38
FIXING AND RESTORING THE SIMULATOR
ALL FIXED, BUT...
NOBODY KNOWS HOW IT WORKS!

## Slide 39
FIXING AND RESTORING THE SIMULATOR
THE PROJECT'S DEPENDENCIES
GWT
AceGWT
THE SIMULATOR

## Slide 40
FIXING AND RESTORING THE SIMULATOR
GWT
Framework (formerly) from Google
Generates web applications (client-server, client only) from Java
Emulates Java's JVM with JavaScript

## Slide 41
FIXING AND RESTORING THE SIMULATOR
GWT
Old, outdated, barely supported
Convoluted custom build tools
Limited emulation of JVM
Basically needs Eclipse plug-in for real development

## Slide 42
FIXING AND RESTORING THE SIMULATOR
AceGWT
Provides GWT bindings for the Ace editor
Can be used like normal GWT component
Also old, outdated, and unsupported

## Slide 43
FIXING AND RESTORING THE SIMULATOR
WORKING IT OUT:
Needed older version of Eclipse, and Eclipse GWT plug-in
Reverse engineered the dependencies and their configuration
Configured build system to stop failing

## Slide 44
FIXING AND RESTORING THE SIMULATOR
AFTER 3 YEARS, WE CAN NOW PRODUCE NEW VERSIONS OF THE SIMULATOR!

## Slide 45
FILLING THE GAPS
Restoration and development of
Arm's Java-based LEGv8 ISA simulator​

## Slide 46
FILLING THE GAPS
WHAT IS THE SIMULATOR MISSING?
Incomplete integer arithmetic
No visualization for the stack memory
No IEEE-754 arithmetic and data instructions

## Slide 47
FILLING THE GAPS
THE MISSING INTEGER-BASED INSTRUCTIONS
MUL – LOWER 64 BITS OF THE MULTIPLICATION
SMULH – HIGHER 64 BITS OF THE SIGNED MULTIPLICATION
UMULH – HIGHER 64 BITS OF THE UNSIGNED MULTIPLICATION
SDIV – SIGNED DIVISION
UDIV – UNSIGNED DIVISION
LDA – LOAD ADDRESS OF A LABEL IN A REGISTER

## Slide 48
FILLING THE GAPS
Easy to implement in the existing codebase
but...
Java doesn't like big or unsigned numbers!

## Slide 49
FILLING THE GAPS
PROBLEM 1
Java does not have primitive 128-bit integer types
The BigInteger library exists
GWT 2.7 doesn't emulate it (2.8 does)

## Slide 50
FILLING THE GAPS
PROBLEM 2
Primitive integers are signed
BigInteger also signed
Bitmask converts 64-bit unsigned integers to 65-bit signed, perform signed operations, back to unsigned

## Slide 51
FILLING THE GAPS
STACK NOT VISUALIZED
Important for testing and debugging complex programs (now we can write them)
Useful to understand LEGv8 and stack management

## Slide 52
FILLING THE GAPS
TAKING SOME INSPIRATION

## Slide 53
FILLING THE GAPS
THE NEW STACK VIEW

## Slide 54
FILLING THE GAPS
ADDING FLOATING-POINT SUPPORT
FADDS, FADDD – ADD TWO IEEE-754 VALUES
FSUBS, FSUBD - SUBTRACT TWO IEEE-754 VALUES
FMULS, FMULD - MULTPLY TWO IEEE-754 VALUES
FDIVS, FDIVD – DIVIDE TWO IEEE-754 VALUES
LDURS, LDURD – LOAD IEEE-754 VALUE FROM MEMORY
STURS, STURD - STORE IEEE-754 VALUE TO MEMORY
FCMPS, FCMPD – COMPARE TWO IEEE-754 VALUES

## Slide 55
FILLING THE GAPS
ARITHMETICAL INSTRUCTIONS
Java's IEEE-754
LEGv8's IEEE-754

## Slide 56
FILLING THE GAPS
MEMORY ACCESS INSTRUCTIONS
Simulator designed for integer use
Memory uses integers to store bytes

## Slide 57
FILLING THE GAPS
IDEA: SEE INTEGERS LIKE RAW BITS
CAN BE USED AS BINARY PROTOCOL
CONVERT FLOATS TO RAW BITS
RETROCOMPATIBILITY!

## Slide 58
FILLING THE GAPS
COMPARISON INSTRUCTIONS
LEGv8 does not specify flag-setting conditions for IEEE-754 comparisons
Use ARMv8's ones:

## Slide 59
FILLING THE GAPS
THE FINAL VIEW

## Slide 60
FILLING THE GAPS
THE CHERRY ON TOP: MODERNIZING THE BUILD SYSTEM

## Slide 61
FILLING THE GAPS
WHY DO THIS?
Latest GWT and AceGWT support Maven
Much easier to include if project also supports Maven

## Slide 62
FILLING THE GAPS
THE TRICKLE-DOWN EFFECT
Libraries are managed automatically
Project decoupled from Eclipse, can use other IDEs or even terminal
Can use Java 21, GWT 2.11
More configurable builds

## Slide 63
CONCLUSIONS
Arm's LEGv8 simulator finally working
Only one to implement every LEGv8 instruction
Can now be developed with modern tools, set-up and build in seconds, much easier collaboration

## Slide 64
THANK YOU FOR
YOUR ATTENTION
THESIS AVAILABLE HERE
SIMULATOR AVAILABLE HERE
: simdeistud